## Slide 1
OSSP HACKATHON 2026 | OPERATING SYSTEMS & SYSTEMS PROGRAMMING
TLB and Page Table Simulator
An Interactive Virtual-to-Physical Address Translation Engine & EAT Performance Analyzer
Complete Project Deliverables
• Working System: Zero-install Web GUI + Python CLI
• Formal Mathematical Model & Effective Access Time
• Multi-policy Cache (LRU/FIFO) & Page Fault Recovery
Key Architectural Capabilities
• 16-bit Bit-level Address Decomposition (VPN & Offset)
• Fully Associative On-Chip TLB Fast-Path (2ns)
• Demand Paging & Automated Workload Benchmarks

## Slide 2
01. PROBLEM STATEMENT & MOTIVATION
The Memory Wall & Address Translation Bottleneck
The Architectural Challenge
• Every memory reference requires translation from Virtual Address to Physical Address.
• Double-Access Penalty: Without hardware caching, reading data requires 2 DRAM cycles (1 for Page Table + 1 for Data).
• Multi-Level Paging: In modern 64-bit systems (4-level page tables), translation latency increases by up to 5x.
• Lack of dynamic educational tools to visualize cache hits, misses, and page faults in real time.
Our Proposed Solution
• Interactive Dual-Environment Simulator (Web GUI + Python CLI).
• Hardware-Accurate TLB Cache: 2ns fast-path query vs 100ns main memory cycle.
• Full Memory State Modeling: TLB table, single-level/hierarchical Page Table, and physical RAM frame pool.
• Live Effective Access Time (EAT) Engine: Quantifies performance gain dynamically across varying locality traces.
• Configurable Hardware Parameters: Page size (256B to 4KB), TLB capacity, and replacement algorithms.

## Slide 3
02. SYSTEM ARCHITECTURE & DATA STRUCTURES
Bit-Level Address Decomposition & Memory Layout
16-Bit Virtual Address Space (64 KB) with Configurable Page Size (e.g., 4096B)
• Virtual Address = [ VPN (Bits 15..12) | Offset (Bits 11..0) ] ➔ VPN = VA >> 12, Offset = VA & 0x0FFF
• Physical Address = (PFN << 12) | Offset ➔ Physical Memory Frame concatenated with exact offset
TLB Cache (SRAM)
• Capacity: 2 to 16 slots
• Fully associative parallel lookup
• Fast latency: 2 ns
• Fields: Tag(VPN), Frame(PFN), Valid, LRU Age, FIFO Order
Page Table (DRAM)
• Complete process address mapping
• In-memory structure: 100 ns latency
• Tracks Valid/Invalid (Present) bits
• Reference and Dirty bit flags
Physical RAM Frames
• 8 Physical Frames (32 KB total)
• Dynamic demand paging allocation
• Frame eviction on memory saturation
• Synchronized TLB flush on eviction

## Slide 4
03. IMPLEMENTATION & REPLACEMENT ALGORITHMS
4-Stage Translation Pipeline & Cache Replacement
The 4-Stage Execution Pipeline
• Stage 1: Address Split ➔ Computes VPN = VA >> k and Offset = VA & Mask.
• Stage 2: TLB Lookup ➔ Checks all associative slots. If Hit ➔ Form Physical Address in 2 ns.
• Stage 3: Page Table Fallback ➔ On TLB Miss (100 ns). If Invalid ➔ Raises Page Fault & triggers Demand Paging (8000 ns).
• Stage 4: Cache Update ➔ Inserts resolved mapping into TLB using selected eviction policy.
Least Recently Used (LRU)
• Tracks monotonically increasing access timestamps.
• Evicts entry with lowest last-used timestamp.
• Optimal for temporal locality loops and stack accesses.
• Highest hit ratios for realistic application workloads.
First-In, First-Out (FIFO)
• Tracks arrival sequence order counter.
• Evicts oldest inserted entry regardless of recency.
• Very low hardware implementation overhead.
• Demonstrates Belady's Anomaly under specific memory access traces.

## Slide 5
04. MATHEMATICAL VERIFICATION & FORMULA
Effective Access Time (EAT) Analysis
Fundamental Mathematical Formulation
EAT = H × (t_TLB + t_MEM) + (1 - H) × (t_TLB + 2 × t_MEM) + (P_fault × t_fault)
• H: TLB Hit Ratio (Hits / Total References) | t_TLB: 2 ns | t_MEM: 100 ns | t_fault: 8000 ns
Baseline Without TLB
• Every reference reads Page Table then Data.
• Latency = 2 × 100 ns = 200 ns.
• Performance degradation: 100% overhead.
• Multi-level paging worsens to 300 - 500 ns.
Optimized With 90% TLB Hit Rate
• EAT = 0.90 × (102 ns) + 0.10 × (202 ns)
• EAT = 91.8 + 20.2 = 112.0 ns.
• Speedup: 1.78x faster than baseline (44% latency reduction).
• Quantitatively proves the hardware efficiency of TLBs.

## Slide 6
05. EXPERIMENTAL BENCHMARKS & RESULTS
Workload Trace Testing & Quantitative Evaluation
High Temporal Locality
• TLB Hit Ratio: 87.5% Hit Ratio | Observed EAT: 114.5 ns EAT
• Context: Tight code loop accessing Pages 1 & 2 repeatedly. High cache reuse.
Sequential Memory Scan
• TLB Hit Ratio: 75.0% Hit Ratio | Observed EAT: 127.0 ns EAT
• Context: Linear array traversal across contiguous pages. Demonstrates spatial locality.
Loop Exceeding TLB (Thrashing)
• TLB Hit Ratio: 0.0% Hit Ratio | Observed EAT: 202.0 ns EAT
• Context: 5-page cycle against 4-slot TLB. Demonstrates catastrophic eviction anomaly.
Uniform Random Access
• TLB Hit Ratio: 12.5% Hit Ratio | Observed EAT: 189.5 ns EAT
• Context: Random memory access across 16 pages with high page fault probability.

## Slide 7
06. CONCLUSION, IMPACT & TEAM RESPONSIBILITIES
Educational Value & Systems Engineering Impact
Team Contributions & Roles
• Member 1: System Architecture, Address bit decomposition algorithms, and EAT mathematical modeling.
• Member 2: TLB cache design, LRU & FIFO replacement engine, Page Table state machine.
• Member 3: Interactive visual dashboard, real-time pipeline animations, responsive CSS styling.
• Member 4: Benchmark workload traces, Python CLI development, test case validation, and documentation.
Summary of Impact
• Dual Deployment: Works as zero-install web app and terminal CLI.
• Bridges Theory & Practice: Brings textbook diagrams to life with interactive address translation.
• Extensible Architecture: Supports configurable page sizes, cache associativity, and latency constants.
• Production-Grade Deliverables: Code, Documentation, PPT Deck, and Live Test Scenarios.
• Ready for Demonstration & Evaluator Q&A.